## Slide 1: Electric Scooter Code and Board Revisions

## Slide 2: Objectives
To improve the start up
To improve the braking
To avoid the unnecessary activation of motor when playing/rocking the electric scooter back and forth without really driving it

## Slide 3: Summary of Changes in the Code
Feature | Description | 
Feature | Released | Updated
Improved Start Up Response from Idle Position | Depends on the simultaneous spinning of wheel and engaging the throttle | Triggered after the wheel spins at 6kph and the throttle is engaged within 1s
Braking | The signal coming from the brake lever is monitored through a digital pin | The signal is monitored through a digital pin and will only be activated when the throttle is disengaged
Securing that the Motor Will not be activated inappropriately | The untimely activation of motor when rolling the electric scooter from standstill does not happen frequently, the released version did not address it. | To ensure that the motor will not be activated mistakenly, changes in getting the count from SCCP peripheral is implemented. The counts from SCCP is used for computing the speed.

## Slide 4: Released Version: Start Up Implementation
The lines of code that enable the motor drive is within the _CNCInterrupt()function.
The measured speed is logically ANDED with the throttle voltage level. The test condition determines if the runMotor and PWM will be enabled.
This method of start up presents no problem when you kicked the scooter hard, because you will gain enough speed, and the algorithm will immediately determine the rotor position.
When you started it without enough speed, since the runMotor and enabling the PWM were done simultaneously, the algorithm cannot readily measure the rotor position causing the rotor to lock.

## Slide 5: Updated Version: Improved Start Up
The lines of code that enables the motor drive is within the _CNCInterrupt() function. If the speed is greater than 6kph(2400), the runMotor test variable is activated.
The algorithm within the _ADCInterrupt() is executed after the runMotor is enabled. The algorithm measures the rotor position, phase current and waits for 1s if the throttle will be engaged.
If the throttle is engaged, the motor runs in Open Loop to avoid the dependency on the measured speed and Closed the Loop after 500 ms.
If the throttle is not engaged, the runMotor is disabled to avoid the wrong timing of enabling the PWM.
The implemented changes allow smooth starting up and guaranteed motor drive.

## Slide 6: Released Version: Braking Implementation
The brake signal coming from the brake lever is sensed through a digital pin.
The voltage level measured during the initial development of the code is lower than 0.2 VDD (about 0.2V), which is within the electrical specification of the pin as shown below.
The braking did not pose any problem during the testing.

## Slide 7: Released Version: Braking Issue
The level of brake signal is directly proportional to the applied brake force or to the intensity of how much you press the lever. The initial measurement was 0.2V to 2.87V, 0.2V as the lowest voltage measured. This level of voltage is read as LOW and did not cause any problem in the initial development.
During the testing of preparing the electric scooter for the tradeshow, an inconsistency is noticed during start-up. After the investigation, it is found out that the brake signal coming from the lever is higher than previously tested (0.87-1V as its minimum and 2.6V to 2.9V as its maximum). It may be a result of the following: wearing out of the lever, loose wiring or even brake construction differences.
The increase in the voltage level across the digital pin activates the regenerative braking early on the stage. For the stated reason, regenerative braking adversely affects the start-up. The issues were solved by implementing changes in the updated version of the code.

## Slide 8: Updated Version: Braking Implementation
The default condition of the electric scooter is OFF, it means that runMotor is disabled, pwmDutycycle is at minimum and PWM drivers are all deactivated.
An additional conditional statement is added for triggering the regenerative braking after disengaging the throttle, to ensure that regenerative braking would not affect the normal driving mode.
Whenever the throttle is disengaged, a counter continually counts until it reached a certain time where it will start the regenerative braking, thus suddenly slow down the motor. After the motor stopped, all the parameters are reset and PWM drivers are disabled.

## Slide 9: Released Version: Continuous Counter for Speed Measurement
The speed measurement function is placed in the _CNCInterrupt(). It uses a 32-bit continuous counter, from which its value is obtain every time a CN Interrupt occurs. The value represents the period between two hall state change. It is the input to the speed measurement function.
During the normal driving operation, the use of continuous counter presents no problem because it accurately measures the speed.
However, when rotating from stop with a very low speed, there are times that the value obtained is high, which leads to a wrong speed calculation. The measured speed value is the basis of turning ON the motor drive. It will not cause an issue if the electric scooter is driven normally(kick and throttle engaged). But, if the motor wheel is rotated at low speed, and the throttle is incidentally engaged, the drive will be enabled falsely.

## Slide 10: Updated Version: Continuous Counter Changes
The SCCP counter is disabled, and its value is reset every time the motor is disabled through the ResetParams()function.
The SCCP counter will be enabled, preloaded with the period of the lowest speed when the _CNCInterrupt() is triggered and the runMotor test variable is disabled.
These changes will not return a wrong speed calculation, if the electric scooter is rotated at low speed. Thus, the runMotor will not be activated mistakenly.